## Slide 1: Deep Learning Models for Accelerating and Enhancing Turbulent Flow Analysis
Group 1
Javad Mortazavian Najafabadi
Christopher J. Abel
Professor: Dr. Hongkai Yu
April 22, 2025

## Slide 2: Outline
Introduction & Problem Statement
  Brief overview of turbulent flow challenges
  Motivation for using deep learning models in CFD
Literature Review
  Summary of previous related works
  Gaps and limitations in current approaches
Dataset Description
  Data source and characteristics
  Preprocessing steps and dataset structure
Problem Formulation & Methodology
  Problem configuration and objectives
  Model architecture and training setup
Preliminary Results & Observations
  Key findings from initial experiments
  Visualizations and performance metrics
Conclusion & Future Work
  Summary of current progress
  Next steps and research directions

## Slide 3: Background & Motivation
Computational Fluid Dynamics (CFD) solves fluid flow problems using numerical methods.
Turbulent flows dominate most real-world fluid scenarios (e.g., biomedical analysis, weather, aircraft aerodynamics, automotive industry, gas & renewable energy turbines).

## Slide 4: Background & Motivation
Direct Numerical Simulation (DNS) of turbulence is accurate but extremely expensive.
Large Eddy Simulation (LES) and RANS offer trade-offs between fidelity and cost.
Turbulent flows are chaotic and multiscale — challenging for traditional solvers.
Deep learning offers a promising alternative for faster, scalable flow predictions.
Source: Journal of Advances in Modeling Earth Systems

## Slide 5: Challenges & Limitations of CFD
High computational expense associated with Computational Fluid Dynamics (CFD) simulations
Finer grid resolutions lead to substantial increases in computational cost and simulation time
Flow field requires extended simulation time to fully develop across the computational domain

## Slide 6: Problem Statement
Why do we want to apply the DL models to the large DNS results databases?
  We aim to develop efficient deep learning models for both estimating the turbulence temporal evolution and performing the super-resolution reconstruction task, thereby reducing the high computational cost of simulations while preserving the accuracy of physical results.

## Slide 7: Literature Review
Background and Brief Timeline of Deep Learning Models in Fluid Velocity Estimation:
Pre-2012:
  Early neural networks were applied to fluid motion estimation (basic pattern recognition, simple velocity extraction tasks).
2012-2017:
  FlowNet (2015): First CNN model (FlowNetS and FlowNetC) introduced for optical flow, providing initial high-resolution velocity estimation capabilities.
  FlowNet2 (2017): Enhanced accuracy by stacking networks, but increased computational cost.
  SPyNet (2017): Coarse-to-fine spatial pyramid approach introduced, reducing model size and computational load.
2018-2019:
  PWC-Net and LiteFlowNet (2018): Employed spatial pyramids with feature warping and cost-volume calculations, achieving good accuracy with moderate computational demands.
  UnLiteFlowNet-PIV (2019): First unsupervised learning approach in fluid velocity estimation based on optical flow networks, reducing reliance on labeled datasets.
2020-2021:
  RAFT (2020): Recurrent neural architecture with iterative refinement (Conv-GRU) providing state-of-the-art accuracy and efficiency.
  PIV-RAFT, RAFT-PIV (2021): Adaptation of RAFT specifically for Particle Image Velocimetry (PIV), significantly improving estimation precision in fluid flows.
  CC-FCN (2021): Integrated traditional cross-correlation methods with fully convolutional networks, enhancing robustness against noise.

## Slide 8: Literature Review
2022-2023 – FlowFormer: Advanced Transformer-based Optical Flow Model
Applications:
  Optical flow estimation using attention-based Transformers.
  Effective in capturing complex global dependencies in turbulent flow data.
Pros:
  Highly accurate due to global attention mechanisms.
  Excellent capability in handling long-range spatial dependencies.
Cons:
  Higher computational and memory costs due to global attention operations.
  Training can be resource-intensive, requiring careful optimization.
  May struggle with very high-resolution flow data without modifications.
Future Improvements for Turbulence Prediction:
  Integrating physics-informed constraints (PINN) to enhance physical interpretability and model accuracy.
  Coupling with recurrent modules (e.g., ConvLSTM) for improved temporal forecasting performance.
Source: Huang, Z., Shi, X., Zhang, C., Wang, Q., Cheung, K. C., Qin, H., ... & Li, H. (2022, October). Flowformer: A transformer architecture for optical flow. In European conference on computer vision (pp. 668-685). Cham: Springer Nature Switzerland.

## Slide 9: Dataset Description
Training and testing datasets: Johns Hopkins Turbulence Database (JHTDB) – https://turbulence.idies.jhu.edu/home
  Direct Numerical Simulations (DNS) of Navier-Stokes
    Isotropic turbulence – turbulence statistics are direction-independent
      1024 x 1024 x 1024 spatial grid
      , saved in 2ms steps from 0 – 10s
    Channel flows – fluid flow between non-slip walls
  At each point (x, y, z, t), the data includes
    Pressure –
    Pressure Gradients (3 components) –
    Velocity (3 components) –
    Velocity Gradients (9 components) –
    Hessians (2nd derivatives – 6 components for , 18 for )

## Slide 10: Dataset Description
Preprocessing steps and dataset structure
  Data Extraction:
    Extract 2D velocity slices (e.g. X-Y) from the original 3D fields
  Normalization:
    Scale velocities min-max or z-score normalization
  Dataset Splitting:
    Define train, validation, and test sets sequentially in time for temporal forecasting.
  Downsampling (if required):
    Reduce resolution from original grids to lower
  Data Augmentation:
    Apply transformations such as flipping, rotation, or shifting to increase training robustness.

## Slide 11: Transforming Data to Images
JHTDB data not stored as images
  Use givernylocal Python library to access data
  Query for specified variable (e.g. , ) over subset of spatial grid points and times
  Capture a snapshot (one ) with one dimension constant (e.g. constant )
  Data for one variable (e.g. vs. )  image
  Save selected points as .csv
dataset = turb_dataset(‘channel5200’, output_path, auth_token)
result = getData(dataset, ‘velocity’, 1.0, ‘none’, ‘lag4’, ‘field’, points)
ux = np.array(result[0])[:, 0].reshape(128, 128)
plt.imsave(‘image.png’, ux, cmap=‘seismic’, vmin=-3, vmax=3)
a
y
x
a
seismic color scheme
min (-3) = blue
max (+3) = red
mid (0) = white
Notes: Chris

## Slide 12: Problem Formulation & Methodology
  Problem configuration and objectives
    Turbulence temporal evolution
      Training the model for 0-8 seconds, testing for 8-10 seconds.
      Exploring the impact of database size, different planes (x-y, x-z, y-z), training epochs, learning rates, etc.
      Exploring different Spatiotemporal Prediction Components (ConvLSTM, GRU, etc.), as well as different Feature Extraction Components.
    Super-resolution reconstruction
      Upscale ux, p from 32 x 32 DNS points in x-y space to 128 x 128 and 256 x 256
      Baseline: explore impact of CNN structure, filter sizes, loss functions on final SNR of upscaled images
      Explore use of multi-path: combine ux and p or combine with gradients to improve final SNR

## Slide 13: Problem Formulation & Methodology
  Model architecture and training setup:
  FluidFlowFormer () Model:
    Inspired by the original FlowFormer
    model
Source
Source
Target
Prediction
ConvLSTM

## Slide 14: Problem Formulation & Methodology
  Evaluation Metrics
    End-Point Error (EPE): The most common loss function and evaluation metric for optical flow estimation problems. It quantifies the accuracy of optical flow predictions by computing the Euclidean distance between the predicted optical flow vectors and the corresponding ground truth flow vectors.
where:
(are predicted optical flow vectors, and ( are the ground truth optical flow vectors.
N is the total number of pixels evaluated.
indexes each pixel location.
    Perceptual Loss: Measures differences between predicted and ground-truth images based on high-level feature maps extracted from pretrained neural networks (usually VGG or ResNet). Unlike pixel-level losses, perceptual loss emphasizes visual quality by comparing structural or textural information.
Where:
and y represent predicted and ground-truth images, respectively.
is a feature extractor (e.g., VGG19 layers).
Minimizing this loss improves realism and visual fidelity.

## Slide 15: Problem Formulation & Methodology
  Evaluation Metrics:
    Gradient Loss: Gradient loss ensures spatial smoothness and structural consistency by comparing the image gradients (edges and structural details) between predicted and target images. This loss reduces visual artifacts by penalizing abrupt spatial variations.
and denote spatial derivatives along x and y directions.
Minimizing this loss leads to smoother and artifact-free predictions.
    Combined Loss:

## Slide 16: Preliminary Results
Trained for 40 epochs, with forecast gap=0.35s
4000 training images with 0.002s timestep, 1000 testing images

## Slide 17: Super Resolution of Fluid Patterns
Goal: CNN Super Resolution of Fluid Images
  DNS solutions of N-S on coarse spatial grid
  “Fill in the blanks” with CNNs
Apply existing CNNs to velocity, pressure images
  SRCNN
  U-Net style networks
Make improvements using fundamental connections between variables
  Use pressure data to enhance SR of velocity
  Use velocity data to enhance SR of pressure
  Incorporate gradients of velocity and pressure
  Gradients can be noisy – pre-process using 2D Savitzky-Golay filter
Notes: Chris

## Slide 18: Use of an SRCNN-Style Network
At right, results of super-resolution of 32 x 32 image of to 128 x 128.
SRCNN network with , training: 377 Isotropic images, 1000 epochs
Further investigation
  Modify SRCNN – , number of channels and layers
  Multi-branch: and , or and
  Alternative loss functions
Ground Truth – 128 x 128 Image
Downsampled to 32 x 32
Super-Resolved to 128 x 128
64 ch
32 ch
C. Dong, C. C. Loy, K. He and X. Tang, "Image Super-Resolution Using Deep Convolutional Networks," in IEEE Transactions on Pattern Analysis and Machine Intelligence, vol. 38, no. 2, pp. 295-307, 1 Feb. 2016, doi: 10.1109/TPAMI.2015.2439281.
Notes: Chris

## Slide 19: Conclusion & Future Works
Summary:
  The Direct Numerical Simulation (DNS) of turbulent fluid flow is computationally expensive; CNNs are a promising supplement to DNS, enabling us to project turbulence patterns in both time and space.
  We proposed a new model called FluidFlowFormer () model inspired by the original FlowFormer model for real-time prediction of the turbulent flow temporal evolution.
  We demonstrated the application of Super Resolution CNNs to project the results of coarse-grid DNS results to a finer spatial grid.
What will be done further:
  Improving the architecture of the proposed FluidFlowFormer () Model by considering the impact of different feature extractors and predictor components.
  Adding a pre-training stage using other planes (i.e. x-z and y-z) to improve the results for the x-y plane.
  Investigate structural modifications to the CNN used for spatial super resolution of fluid patterns
  Investigate multi-path CNNs with parallel velocity / pressure or velocity / velocity gradient input pairs for super resolution

## Slide 20: Backup Slides

## Slide 21: Geometry
Turbulent fluid flow between parallel plates
Unit vectors as shown
  along direction of flow (streamwise)
  normal to walls
  across flow (spanwise)
Focusing on the velocity in the direction of the flow (), as this will dominate the overall velocity
Plates are “non-slip” -- at
J. Kim, P. Moin and R. D. Moser. Turbulence statistics in fully developed
channel ow at low Reynolds number. J. Fluid Mech., 177:133-166, 1987.
1
-1
Side View
Flow
Slice in XY plane (z = midline)
Notes: Chris

## Slide 22: Dataset Description
Data source and characteristics
  Forced Isotropic Turbulence Database Simulation parameters:
    Domain: 2 x 2 x 2 (i.e. range of x1 , x2 and x3 is [0, 2])
    Grid:
    Viscosity ( ν ) = 0.000185
    Simulation time-step Δt = 0.0002
    Data are stored separated by t = 0.002 (i.e. every 10 DNS time-steps is stored)
    Time stored: between t=0 and 10.056 (5028 time samples separated by t)